## Slide 1
The Rocket Men
Project One Giant Leap

## Slide 2: Dimensions
Rocket Length- 81.95 in.
Rocket Mass- 171 oz.
Top Body Tube Length- 27.7 in.
Bottom Body Tube Length- 36.0 in.
Cone Length- 16.75 in.
Body Tube Inner Diameter- 3.902 in.
Body Tube Outer Diameter- 4.094 in.
Static Stability Margin- 2.51 cal.

## Slide 3: Materials for Rocket
Plastic Nose Cone
Fiberglass-wrapped Phenolic Body Tube
2.152” Motor Mount Tube
G10 FR4 Fiberglass for Fins
West Systems Epoxy
½ inch Plywood Centering Rings and Bulkheads
Spray Paint

## Slide 4: Materials for Recovery System
  PerfectFlite StratoLogger Altimeter
Altimeter USB Data Transfer Kit
9 Volt Batteries for Altimeters
Electronics Arming Switch- Key Switches-
Type 3
3.9” Electronics Bay
Terminal Strips for Ejection Charges
15” Drogue Parachute
72” Iris Ultra Main Parachute

## Slide 5: Materials for Recovery System Cont.
1”x25’ Tubular Nylon Shock Cord 4,200 lb. Test
30” of Kevlar Shock Cord Protector
½ inch Eyebolts
Quick Links

## Slide 6: Materials for Payload Component
  Datalogger- USB Current and Voltage Datalogger
  3 Volt Lithium Battery for Datalogger
  ¼ inch Plywood for Bulkheads and Centering Ring
  Wooden Supports
  PT-3.0 Phenolic Tubing
  Diode and Resistor
  Memory Foam
  Clear Cast Acrylic- Lucite Cylinder
  Flexible Solar Panel
  Wires

## Slide 7: Plan for Vehicle Safety Verification and Testing
Bulkhead Testing
Ejection Charge Testing
Recovery System Harness Testing

## Slide 8: Baseline Motor Selection and Justification
Cesaroni Technology Inc. K2045 Vmax motor
54mm in diameter
16.0 in. in length
1417 Newton-seconds of impulse
Justification
  Commercial Availability
  Design Compatibility
  Affordability
  Rail Exit Velocity

## Slide 9: Thrust-to-Weight Ratio and Rail Exit Velocity
Thrust-to-Weight Ratio (T/W)- 43.0
Rail Exit Velocity- 148ft/s

## Slide 10: Launch Vehicle Verification and Test Plan Overview
Recoverability and reusability of the Rocket
Launch Configuration Sustainability
Recovery System Functionality

## Slide 11: Drawing/Discussion of Each Major Component and Subsystem
Airframe
Recovery
Payload

## Slide 12: Airframe
Nose Cone
Top Body Tube
Bottom Body Tube
Electronics Bay
  acts as a coupler
Bulkheads
Fins

## Slide 13: Recovery
Dual Deployment
  Drogue Parachute
  Main Parachute
Electronics Bay
  Redundant Altimeters

## Slide 14: Recovery Cont.
Altimeters
Ejection Charges
Arming Switches

## Slide 15: Payload
Payload Objective
Payload Description
    Structure
    Electronics

## Slide 16: Baseline Payload Design

## Slide 17: Baseline Payload Design Cont.
Flexible Solar Panel
Lucite Cylinder
Electronics
Datalogger

## Slide 18: Payload Verification and Test Plan Overview
Collection and Analysis of the Payload Data
Recoverability and Reusability of the Payload